## Slide 1: Arduino “BLI” monochromator controller – peripheral hardware setup for OBB
Copyright 2026 Andrew B. Greytak, University of South Carolina – Documentation shared via CC-BY-SA-4.0
https://github.com/Greytak-Chemistry-Lab/arduino-bli-mono-controller/LICENSE
A professionally-built setup with NEMA-23 stepper motor. Includes shutter solenoid (H-1079-032 1208, probably 12V) and optical limit switch.
Motor part number: Kollmorgen P21NRXS-LNN-NS-17
Our home-modified setup with NEMA-17 1.5Amp stepper motor (Twotrees). Employs mechanical limit switch (WELWIK 3-pin end stop switch for 3D printers).
Repurposed Optical Building Blocks (OBB) monochromators (table is 1” grid)
3D printed adapters for paddle and switch mount
3D printed adapter for motor mount
reducing flexible shaft coupler 6.35 mm (1/4 inch) to 5 mm

## Slide 2: Parts list
Part | Part Number / Supplier | Note
Stepper motor NEMA-17 1.5 amp | 17HS4401 / Twotrees (Amazon) | No longer available from this vendor, but part# is standard
Limit switch (3-pin end stop switch) | WELWIK (Amazon) | 
Limit switch cable (1M XH2.54 3PIN Cable Endstop Switch Wire) | GRGRG (Amazon) | XH2.54 male/male
Stepper motor cable 4pin to 6pin, 1.5 M | TIEXYE (Amazon) (Compatible with NEMA 17 for Ender 3 printer) | XH2.54 mm 4pin male / PH 2.0 6pin male
6.35mm (1/4”) shaft coupler | Twidec 6.35 mm rigid coupler | Blue aluminum part in photo
Flexible reducing coupler | Xnrtop 5mm to 6.35 mm aluminum | 
Limit switch paddle | Gryphon Drake designs “IR spectrometer limit switch” assembly (Accessible on Greytak Chemistry Lab Onshape space) | Attaches to moving part
Limit switch mount | Gryphon Drake designs “IR spectrometer limit switch” assembly | Bolts to instrument floor
Motor mount | GDD “spectrometer motor bracket” | 
Grating 50x50x6 mm | Newport 33010FL01-520R | For NIR: 600 lines/mm blazed 1.02 um, blaze angle 17.46 degrees
3D designs copyright 2024 Gryphon A. Drake
Documentation Copyright 2026 Andrew B. Greytak, University of South Carolina – Documentation shared via CC-BY-SA-4.0
https://github.com/Greytak-Chemistry-Lab/arduino-bli-mono-controller/LICENSE