## Slide 1
We should define directions in wavelength = LONGER or SHORTER and then use #define to specify which of these is clockwise or counterclockwise for motor rotation.
We can debounce by polling switches with a 100-200 ms “HOLDOFF” delay
All motor motions will be a loop in which only as many steps as can be done in HOLDOFF are carried out before checking switch input values.
We will mainly keep track of progress with position variable as integer number of nm. A subroutine will calculate the change in Steps necessary for every move of nm, and LCD will be updated each move loop iteration.

## Slide 2
setup()
loop()
if initialize (home) flag is set (first run, or commanded):
if autoManual true, manual mode
if automanual false, auto mode
1. auto run setup: Display and update settings
2. auto run: Main Loop
3. auto run: Scan loop
Power on; possible separate power switch for motor/driver output to enable it to be shut off / cooled without resetting Arduino
Setup pins, LCD
Set motor speed
positionSteps()
Returns the number of steps from home to reach a desired wavelength position in nm, based on lookup table or calibration function
moveSteps()
Move a number of steps forward or backward at the desired speed while polling limit1, limit2/stopreset
Subroutines:
Ask user if we should initialize; possibly other config options
If commanded, initialize: run backward until limit switch, then forward slow to disengage limit switch, then define position and run forward to starting position target; un-set initialize flag
position_target loop: user selects position target; startnext or autoManual to break out
check flags
if new position was selected, move until correct position
check flags
Get start, end, speed, number of scans; break on automanual
Check flags
If not at starting position, Move backwards to start, including backlash corr. Check flags. Display ready.
do while # scans is not completed:
Blink LED / TTL out
Move forwards to end
Check flags
Return to starting position, with backlash corr.
Display scan complete
Check flags
Wait on start key, break on stopreset or autoManual
Possible Subroutines:
resetPress()
A possible subroutine to start a counter when reset is pressed and check if it is held down a long time, prompting initialize flag to be set